## Slide 1: EDES 301 Reaction Tug-of-War Proposal
10/01/2026
Jordyn Mariam

## Slide 2: Background Information
What is being proposed?
  A 2-player reaction game on the PocketBeagle
    After a random “GO” cue, whoever reacts first and hits their button first pulls a light on an LED-strip “rope” one step toward their side
    First player to pull the rope to their end wins
    The display will show each round’s reaction time
      Possibly build in a punishment if react too early (move one step towards the opponent)
Improvements / additions over existing project
  This game was inspired and builds on the Whac-a-Mole Game with PocketBeagle (Welsh & Wicks, Hackster.io)
  Libraries: Adafruit_BBIO (GPIO, PWM, ADC), HT16K33 7-segment driver, spidev (WS2812 LED strip over SPI)
  From 1 player chasing a score  2 players head-to-head (maybe add a 1-player mode)
  4 single LEDs  addressable LED strip “rope”
  Hit/miss scoring  millisecond reaction timing with first-press detection
  New: false-start penalty, best reaction stats saved across reboots
My story:
I originally was going to focus my project on something to help with studying, but I instead decided I wanted to do something more fun . I wanted to build upon Whac-a-Mole by making it a head-to-head game that can be played with my friends and family to hopefully illustrate all that I’ve learned in EDES 301.
Notes: My project is a two-player reaction tug-of-war game. After a random GO cue, whoever hits their button first pulls a light on an LED strip one step toward their side, and the first to pull it all the way wins. The 7-segment display shows reaction times in milliseconds. It builds on your Whac-a-Mole project. I'm taking it from one player chasing a score to two players head-to-head, replacing the 4 LEDs with an addressable, LED strip and adding millisecond timing and a false-start penalty.
If need to broaden scope: single-player mode against a computer

## Slide 3: System Block Diagram
Notes: Left side, inputs:
Two arcade buttons, one per player, plus a start button. Each is a GPIO connection.
Difficulty knob (potentiometer) uses AIN, an analog input. Reads how far the knob is turned. Likely will be used for single-player mode: sets how fast the computer “reacts.”
The micro-USB connector brings power in (the red line)
Right side, outputs:
7-segment display, over I2C. A two-wire conversation where the PocketBeagle sends numbers to show.
LED strip, over SPI: a fast data line that tells each LED what color to be. Goes through a level shifter first because PocketBeagle speaks at 3.3V and the strip expects 5V.
Buzzer, over PWM: the pin switches on and off very fast, and the speed sets the pitch of the sound.
µSD card: where Linux, code and saved stats live.
timestamp each press when it happens, using edge detection, instead of checking the buttons one after another in a loop

## Slide 4: Power Block Diagram
Notes: Power comes in from a 5V wall adapter through the micro USB port
Pocketbeagle hands it out on three rails
  5V (red) for the LED strip
  3.3V (blue) for the display, buzzer, and buttons
  1.8V (green): only for difficulty knob. The analog input can’t handle more than 1.8V, so the knob must be wired here
Led is the main power draw so I’ll cap brightness in the software and use a 2 A wall adapter
How do you recommend controlling the LED strip from the PocketBeagle?

## Slide 5: Components / Budget
Component | EDES301 to Buy? | Cost
PocketBeagle, jumper wires | No | In Kit
4-digit, 7-segment display w/I2C backpack | No | In Kit
Buzzer, potentiometer, button | No | In Kit
Addressable LED strip (WS2812B, small strips) [Amazon link] | Yes | $17.99
Level shifter (1 in 5 pack) [Amazon link] | Yes | $1.60
Arcade buttons (not necessary but fun add) x 2 [Adafruit link] | Yes | $11.90
5 V / 2 A USB wall adapter | No | I own
Total purchasing cost: |  | $31.49
Notes: Will the parts-list level shifter (pocketbeagle’s pins put out 3.3 V, and the LED strip expects a 5 V data signal) be fast enough for the LED strip?
Are the arcade buttons OK or should I just use the kit buttons?
Instead do a row of the kit LEDs as a rope?
Potentiometer  difficulty

## Slide 6: Software Block Diagram
TugOfWarGame
tug_of_war.py
State: rope position, mode, difficulty, round start time, best times
_setup() – create + initialize all drivers
run() – main loop (see flow diagram)
select_mode() – 1P vs CPU or 2P
play_round() – random wait, GO, judge
false_start(player)
cpu_reaction_ms() – from difficulty
victory(player)
cleanup() – on Ctrl-C
Python libraries used:
Adafruit_BBIO (GPIO, ADC, PWM), spidev,
smbus (I2C), time, random, json
USER OUTPUTS
PlayerButton (P1)
player_button.py → extends Button
GPIO P2_02
get_press_time()
PlayerButton (P2)
player_button.py → extends Button
GPIO P2_04
get_press_time()
Button (start / mode)
button.py (HW #4)
GPIO P2_06
wait_for_press()
get_last_press_duration()
Potentiometer
potentiometer.py (class)
AIN0 P1_19
get_value() → 0–4095
HT16K33
ht16k33.py (class)
I2C1 – 7-seg display
update(ms)
text('rdy')
Rope
rope.py
game view of LED strip
draw(position)
flash() win_anim()
Buzzer
buzzer.py (PWM)
PWM1A P2_01
play(freq, length)
StatsStore
stats.py
JSON file on µSD
record(p, ms)
get_best() save()
LEDStrip
led_strip.py (WS2812 via spidev)
SPI0 MOSI P1_12
set_pixel() show()
Already written (class / homework)
To be written for this project
Blue text = API calls between classes

## Slide 7: Classes and HW API
Class | File | Status | Functions (preliminary API) | Purpose
TugOfWarGame | tug_of_war.py | To write | _setup(), run(), cleanup(), select_mode(), play_round(), false_start(p), cpu_reaction_ms(), victory(p) | Main program and game logic
PlayerButton | player_button.py | To write (extends Button) | arm(), disarm(), was_pressed(), get_press_time() | Timestamps each arcade-button press with GPIO edge detection so the first press wins fairly
Button | button.py | Done (HW #4) | is_pressed(), wait_for_press(), get_last_press_duration() | Start / mode button (short press = 2P, hold > 2 s = 1P)
Potentiometer | potentiometer.py | Done (class) | get_value() | Difficulty knob (CPU speed)
HT16K33 | ht16k33.py | Done (class) | clear(), blank(), update(value), text(str) | Reaction time, “rdy”, winner (P1 / P2)
LEDStrip | led_strip.py | To write | set_pixel(i, color), fill(color), show(), clear(), set_brightness(b) | WS2812 driver over SPI (spidev); brightness capped
Rope | rope.py | To write | draw(position), flash(color), win_animation(player), idle() | Turns rope position into LED patterns
Buzzer | buzzer.py | To write | play(freq, length), stop() | GO beep, false-start buzz, victory tune
StatsStore | stats.py | To write | load(), save(), record(player, ms), get_best() | Best reaction times / wins saved across reboots
Notes: Also: configure_pins.sh (I2C, SPI, PWM, GPIO pins) and run script → started at boot by cron

## Slide 8: SW Flow Diagram
Main Program
Setup
display.clear() stats.load()
Wait for Start
start.wait_for_press()
New Game
get_last_press_duration() pot.get_value()
Play Round
Move Rope
rope.draw(pos) display.update(ms)
Check Rope
Victory
rope.win_animation() stats.save()
Power up
No press
Time < 2s → 2P Time > 2s → 1P
At end
Not at
end
Ctrl-C (any state)
→ cleanup()
Play Round
Ready
random 1–4 s wait p1/p2.arm()
GO!
buzzer.play() rope.flash()
Wait for Press
p1/p2.was_pressed()
Pick Winner
get_press_time() cpu_reaction_ms()
Wait over
Press (or CPU)
No press
False Start
rope moves toward
other player
Pressed early
Retry
Cleanup
Execute Task
run()
Cleanup
display.text('----')
strip.clear() stats.save()
Ctrl-C